## Slide 1: Advanced Topics in Computer Networks Capture & Decode LoRa Signals
Iliadis Ilias 2523 Lamprinos Isidoros 2551

## Slide 2: LoRa characteristics
What is LoRa?
  Low-power wide-area network modulation technique
It provides long-range communications
Accommodates vast range of IoT applications

## Slide 3: LoRa frequency bands
Europe: 433MHz and 868MHz
Australia and North America: 915MHz
Asia: 923 MHz

## Slide 4: Identify Transmission Frequency
The device we used in order to implement this project is Adalm-Pluto SDR
Used Blocks:
QT GUI Waterfall Sink
QT GUI Frequency Sink

## Slide 6: Demodulating Captured Signals
Schema used for real time LoRa signal demodulation

## Slide 7: Modulation Parameters
Coding Rate(CR):
  Amount of redundant bits added for error correction(FEC)
Bandwidth(BW):
  Frequency Width
  Higher BW Higher Data Rate, Lower Sensitivity
Spreading Factor(SF):
  SF range: 7-12
  Larger SF Higher processing Gain , Longer Transmission Rang

## Slide 8: LoRa Transmission Modes (1/2)

## Slide 9: LoRa Transmission Modes (2/2)
We manually changed the SF and BW in order to find the current transmission mode

## Slide 10: Dynamic Implementation
This GRC schema is the one we used to produce the python file that we used to implement the dynamic algorithm of our project.

## Slide 11: Decoding
Listening to port 40868 for 20”
  If no data captured change mode
  Else continue listening
Get source IP address and port from msg[1]
Unhexlify data and search for delimiters

## Slide 12: Experiment Results
On modes 8,9,10 BW is set to 500kHz and corrupted packets are frequently observed. For modes 8,9 distance between receiver and transmitter affects the packet correctness.
In mode 6 we seldom observe any transmission.
Modes with BW 250kHz and mode 3 with BW 125kHz are the most reliable for correct transmission.
In mode 1 if the distance between transmitter and receiver is lower than 1.5m no transmission is detected.

## Slide 13: Future Work/LoRa Transmitter

## Slide 14: Thank you for your attention
Any Questions?